OpenParEM3D
Electromagnetic Simulator
Brian Young
January 9, 2024

---
Agenda
- Motivation
- Features
- S-parameters
- 3D FEM setup
- Adaptive mesh refinement
- Examples and discussion
- Regression suites
- Conclusion

---
Motivation
- Lack of a free or very low-cost frequency-domain S-parameter electromagnetic simulator inhibits exploration of new ideas and development of new products
- Target audience
  - Engineers wanting to explore ideas at home
  - Continuing education
  - Students
  - Small startups
- Feasibility
  - Leverage existing open-source projects
  - CAD (FreeCAD), meshing (gmsh), FEM (MFEM), visualization (ParaView)
  - “Just” need to glue it all together

---
Features
- Full-wave time-harmonic 3D electromagnetic simulator
- Computing
  - Electric and magnetic fields
  - S-parameters between 2D ports on the surface of the 3D space
- Arbitrary high-order elements
  - courtesy of MFEM, ParaView [up to 6th order]
- Parallel processing via MPI
  - courtesy of MFEM, PETSc, and SLEPc plus custom code
- Adaptive mesh refinement
  - courtesy of MFEM plus custom code
- TBD: impedance boundary condition for conductor losses and antennas

---
S-parameters
- “S-parameters” is short for “scattering parameters”
  - Links incident and reflected waves at the ports of a 3D volume
- Dominant in engineering to include electromagnetic results in circuit simulations and for performance analyses
- A “must have” output for a practical simulator

---
S-parameter Matrix Extraction
S-parameter matrix
size *2 {color white {left [ stack{b rsub{1} # b rsub{2} # alignc dotsvert # b rsub{N} } right ]=left [ matrix{S rsub{11} # S rsub{12} # dotsaxis # S rsub{1N} ## S rsub{21} # S rsub{22} # dotsaxis # S rsub{2N} ## dotsvert # dotsvert #dotsdown #dotsvert ## S rsub{N1} # S rsub{N2} # dotsaxis # S rsub{NN}} right ] left[ stack{a rsub{1} # a rsub{2} # dotsvert # a rsub{N}} right ]}}
Propagating waves are modes on transmission lines or waveguides feeding N ports.
a1
Port 1
b1
- Define ports - 2D (flat) on surface of 3D space
- Solve 1 column at a time
  - Drive port i such that ai ¹ 0
  - Apply absorbing boundary condition on all other ports, then ak = 0 for k ¹ i
- Solve the 3D problem N times for i=1,..,N
- Separate ai and bi at the driven port
- Output frequency-dependent S-parameters in Touchstone file format
a2
Port 2
b2
aN
Port N
bN
ai is the incident wave to port i
bi is the reflected wave from port i

---
Driving ai
Port i: 2D simulation for fields, a, b, Zo
- MFEM’s ParSubMesh functionality is used to extract 2D meshes
- A 2D simulation is run for each port with OpenParEM2D*
- The 2D field solution for port i is applied to the 3D space, forcing the 3D fields at the port to take the 2D configuration
- An absorbing boundary condition is applied at the other ports
- 3D electromagnetic simulation is run
- Repeat for each port
- Extract S-paramters (more later)
Port k: absorbing boundary
* OpenParEM2D was presented at the
  2022 MFEM Community Workshop.

---
3D FEM Setup
Weak form of the wave equation in E
Separate the surface integral
size *2 { color white {iiint rsub{%OMEGA} {1 over %mu rsub{r} nabla times overline E cdot nabla times overline W dV} - k rsub{0} rsup {2} iiint rsub {%OMEGA} {%epsilon rsub{r} overline E cdot overline W dV} + iint rsub{S} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS} = 0}}
MFEM
CurlCurlIntegrator
MFEM
VectorFEMassIntegrator
Surface of the 3D space
size *2 { color white {iint rsub{S} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS} = iint rsub{S rsub{b}} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS} + sum csub{i=1} csup{N}{iint rsub{S rsub{pi}} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS}}}}
N ports
PEC and/or PMC boundary
Apply BC directly to the matrix
[DOF=0 for PEC, keep DOF for PMC]

---
2D Port Setup on Surface
Setup of the surface integral (from prior slide)
- Apply a propagating assumption at the ports
  - A first-order absorbing boundary condition
size *2 { color white {iint rsub{S} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS} = iint rsub{S rsub{b}} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS} + sum csub{i=1} csup{N}{iint rsub{S rsub{pi}} {1 over %mu rsub{r} hat n times nabla times overline E cdot overline W dS}}}}
DOF manipulation
Not Supported in MFEM
size *2 { color white {matrix{ hat n times nabla times overline E # "=" # `- {{partial overline E_t} over {partial n}} + nabla_t E_n ## "" # "=" # %gamma overline E_t + nabla_t E_n}}}
Identity
size *1.5 {color white {{partial overline E rsub{t}} over {`partial n}={partial overline E(t)func e^{-%gamma n} rsub{t}} over {~~~~partial n} = - %gamma overline E(t)}}
Propagation
Assumption
Not supported in MFEM for Nedelec elements
Normal component on the boundary
Assume that this term is negligible
MFEM
VectorFEMassIntegrator

---
On the Neglected Gradient Term
- On the port boundaries, the gradient term of the normal component is neglected
- A zero gradient of a non-zero En is not physically realizable
  - This means that it is assumed that En=0
- The implemented boundary condition strictly only applies to transverse electric modes (TE and TEM)
  - TE and TEM cases dominate problems of interest. These include microstrip, stripline, coax, triax, slot line, coplanar waveguide, the TE10 mode in rectangular waveguide, and generally, any N-conductor transmission line
  - So the TE restriction in practice is not significantly limiting
- Non-TE modes suffer field distortion at the port leading to a reflection
- Non-TE modes at the boundaries can be supported by using TE modes at the ports with 3D transitions to the required non-TE ports followed by de-embedding (like lab measurements)
- For quasi- TE and TEM modes, En is small compared to Et
  - The error caused by the reflection is determined by the strength of En
  - For quasi- TE and TEM modes, the reduction in accuracy may be acceptable
- Future work is needed to relax this restriction, for example, by including the gradient term or by implementing a perfectly matched layer (PML) boundary condition

---
Top-Level Implementation Details
Start Here
2D ParMesh
ports
ParMixedBilinearForm
→ HypreParMatrix
ParSubMesh
methods
3D ParMesh
color white {left[ {matrix{ alignc "-" # alignc "-" # dotsaxis # alignc "-" ## alignc "-" # alignc "-" # dotsaxis # alignc "-" ## alignc dotsvert # alignc dotsvert # dotsdown # alignc dotsvert ## alignc "-" # alignc "-" # dotsaxis # alignc "-" }} right]}
Re
OpenParEM2D
hypre_ParCSRMatrixToMat()
Custom system construction
Apply known port DOFs
Apply PEC BC
Form linear system
color white {left[ {matrix{ alignc "-" # alignc "-" # dotsaxis # alignc "-" ## alignc "-" # alignc "-" # dotsaxis # alignc "-" ## alignc dotsvert # alignc dotsvert # dotsdown # alignc dotsvert ## alignc "-" # alignc "-" # dotsaxis # alignc "-" }} right]}
PETSc Mat
color white {left[ {matrix{ alignc "-" # alignc "-" # dotsaxis # alignc "-" ## alignc "-" # alignc "-" # dotsaxis # alignc "-" ## alignc dotsvert # alignc dotsvert # dotsdown # alignc dotsvert ## alignc "-" # alignc "-" # dotsaxis # alignc "-" }} right]}
Im
complex
Complex Ax=b solve in PETSc*
frequency domain is inherently complex
MFEM does not support complex
Custom fill of Re and Im ParGridFunctions
Solve for H and fill Re and Im ParGridFunctions
[Similar flow as for E]
Solve S-parameters
Export for ParaView
* A real formulation was tried in MFEM, but poor convergence was observed. For background, see David Day and Mike Heroux, “Solving
   Complex-valued Linear Systems via Equivalent Real Formulations”, report from Sandia National Laboratories, May 9, 2000. There is a
   later SIAM paper based on this work.

---
Sii: Separating ai and bi
- At this point, the 3D fields for E and H are computed.
  - The E-field from the 2D port simulation was applied at port i [i.e. the driving port]
  - Cannot differentiate E+ from E- just from the port i E-field.
  - Requires H to separate the two
- Just use the tangential components since they dominate in practical applications

---
At Port i, the Driving Port
size *2 {color white {overline E rsub{ti}=C rsub{1i} overline E rsup{"+"} rsub{ti} + C rsub{2i} overline E rsup{"-"} rsub{ti} }}
Split with weights
Inner products
supported by MFEM
size *2 { color white { iint rsub{S rsub{i}} overline E rsup{"-*"} rsub{ti} cdot overline E rsub{ti} dS = C rsub{1i} iint rsub{S rsub{i}} overline E rsup{"-*"} rsub{ti} cdot overline E rsup{"+"} rsub{ti} dS + C rsub{2i} iint rsub{S rsub{i}} overline E rsup{"-*"} rsub{ti} cdot overline E rsup{"-"} rsub{ti} dS }}
size *2 {color white {overline E rsup{"-"} rsub{ti} = overline E rsup{"+"} rsub{ti} }}
size *2 { color white { iint rsub{S rsub{i}} overline E rsup{"+*"} rsub{ti} cdot overline E rsub{ti} dS = C rsub{1i} iint rsub{S rsub{i}} overline E rsup{"+*"} rsub{ti} cdot overline E rsup{"+"} rsub{ti} dS + C rsub{2i} iint rsub{S rsub{i}} overline E rsup{"+*"} rsub{ti} cdot overline E rsup{"+"} rsub{ti} dS }}
size *2 { color white { e rsub{0i}=(C rsub{1i} + C rsub{2i} ) e rsub{2i} }}
size *2 {color white {C rsub{1i}=1 over 2 left(e rsub{0i} over e rsub{2i} + h rsub{0i} over h rsub{2i} right) }}
size *2 {color white {overline H rsub{ti}=C rsub{1i} overline H rsup{"+"} rsub{ti} + C rsub{2i} overline H rsup{"-"} rsub{ti} }}
Same mode, same weights
size *2 {color white {C rsub{2i}=1 over 2 left(e rsub{0i} over e rsub{2i} - h rsub{0i} over h rsub{2i} right) }}
size *2 { color white { iint rsub{S rsub{i}} overline H rsup{"-*"} rsub{ti} cdot overline H rsub{ti} dS = C rsub{1i} iint rsub{S rsub{i}} overline H rsup{"-*"} rsub{ti} cdot overline H rsup{"+"} rsub{ti} dS + C rsub{2i} iint rsub{S rsub{i}} overline H rsup{"-*"} rsub{ti} cdot overline H rsup{"-"} rsub{ti} dS }}
size *2 {color white {overline H rsup{"-"} rsub{ti} = - overline H rsup{"+"} rsub{ti} }}
Note the change in sign
size *2 { color white { iint rsub{S rsub{i}} overline H rsup{"+*"} rsub{ti} cdot overline H rsub{ti} dS = C rsub{1i} iint rsub{S rsub{i}} overline H rsup{"+*"} rsub{ti} cdot overline H rsup{"+"} rsub{ti} dS - C rsub{2i} iint rsub{S rsub{i}} overline H rsup{"+*"} rsub{ti} cdot overline H rsup{"+"} rsub{ti} dS }}
size *2 { color white { h rsub{0i}=(C rsub{1i} - C rsub{2i} ) h rsub{2i} }}

---
Sii
- E+ is the +z direction in OpenParEM2D
  - Away from the 3D space, so related to b
  - E- is then related to a
- Voltage wave relationships to S:
Proportional to the weights:
(field structure is the same)
Sii:
size *2 { color white { a rsub{i} ` = ` {```V rsub{i} rsup{"+"}} over sqrt{Z rsub{oi}} }}
size *2 { color white { b rsub{i} ` = ` {```V rsub{i} rsup{"-"}} over sqrt{Z rsub{oi}} }}
size *2 { color white { b rsub{i} ` = ` {```C rsub{1i}} over sqrt{Z rsub{oi}} }}
size *2 { color white { a rsub{i} ` = ` {```C rsub{2i}} over sqrt{Z rsub{oi}} }}
size *3 {color white {S rsub{ii} ` = ` b rsub{i} over a rsub{i} = left( {e rsub{0i} over e rsub{2i} + h rsub{0i} over h rsub{2i} } right) / left( {e rsub{0i} over e rsub{2i} - h rsub{0i} over h rsub{2i} } right) }}

---
Sji
Use direct calculation with voltages*
Sji:
size*2 {color white { V rsub{j} rsup{"+"}=V rsub{j} }}
Integrate at the output port (no reverse wave):
Integrate at the input port, then take the fraction traveling towards the 3D space:
size*2 {color white { V rsub{i} rsup{"-"}=C rsub{2i} V rsub{i} }}
size *2 {color white {S rsub{ji} ` = ` b rsub{j} over a rsub{i} = left( {V rsub{j} rsup {"+"} over sqrt{Z rsub{oj}}} right) / left( {V rsub{i} rsup{"-"} over sqrt{Z rsub{oi}}} right) }}
Use power/voltage definition for Zo
size *3 {color white {S rsub{ji} ` = ` b rsub{j} over a rsub{i} = left( {V rsub{j} over sqrt{Z rsub{oj}}} right) / left( {{C rsub{2i} V rsub{i}} over sqrt{Z rsub{oi}}} right) }}
* Can also use currents, which is a future upgrade, to enable the power/current definition of Zo.

---
Adaptive Mesh Refinement (AMR)
- Follows the setup used in the MFEM Tesla miniapp
  - CurlCurlIntegrator on E, RT elements for flux, and ND elements for smoothed flux
  - Merge errors from both Re(E) and Im(E)
- Extract errors from several solutions
  - Per driven port
  - Combine across all driven ports
  - Apply threshold refinement with a cap on the number of elements to refine
- Refine using ParMesh::GeneralRefinement
- Convergence test is on S. Calculate an error criteria at the Nth iteration
  - error=max column norm {SN-1(SN-SN-1)}
- Options for sequential number of iterations that must meet the convergence criteria
- Options for AMR at multiple frequencies
- Issue? Degradation of mesh quality with each iteration, especially at ports

---
Examples and Discussion

---
WR90 Loaded Rectangular Waveguide
- Exact solution
  - |S11| in dB → -∞
  - phase shift from high-
  1. resolution OpenParEM2D simulation
High accuracy with regular improvement to a very low noise floor
Port 2
Port 1
air
Re(Ey)
Teflon
8.3 GHz
max edge length = 0.825 ג

---
h-Convergence with AMR
- WR90 loaded rectangular waveguide at 8.3 GHz
- Effective AMR
- Accuracy improves with AMR and FEM order
- Favor FEM order over iterations

---
WR75 with Dielectric Puck
Port 2
- Solve with and without AMR
  - 2nd order, AMR: 575 s
  - 4th order: 968 s
- Excellent agreement between runs with and without AMR
- Excellent agreement between this and prior work
Port 2
air
Port 1
size *1.5 {color white {%epsilon rsub{r}=6}}
Refinement focussed on the puck
at 10 GHz
No AMR: max edge length = 0.825 ג
AMR: max edge length = 0.230 ג
refine
refine
Re(|E|)
K. Ise, K. Inoue, and M. Koshiba, “Three-Dimensional Finite-Element Solution of Dielectric Scattering Obstacles in a Rectangular Waveguide,” IEEE Trans. Microwave Theory and Techniques, vol. 38, no. 9, Sept. 1990, pp. 1352-1359.
K. Hirayama, Md. Alam, Y. Hayashi, and M. Koshiba, “Vector Finite Element Method with Mixed-Interpolation-Type Triangular-Prism Element for Waveguide Discontinuities”, IEEE Trans. Microwave Theory and Techniques, vol. 42, no. 12, Dec. 1994, pp. 2311-2316.
Port 1

---
WR75 Waveguide T-Junction
Port 1
- WR75 lossless waveguide splitting to two half-height waveguides for an even power split
- 4th order elements with no adaptive refinement
- Excellent agreement between this work and the referenced paper
Re(Hx)
12.5 GHz
max edge
length = 0.245 ג
Port 3
Port 2
F. Alessandri, M. Dionigi, and R. Rorrentino, “Rigorous Analysis of Compensated E-plane Junctions in Rectangular Waveguide,” 1995 IEEE MTT-S Digest, pp. 987-990.

---
Microstrip Bridge
- Microstrip on GaAs bridging across a gap through a block of variable dielectric constant material
- 5th order elements with no adaptive refinement
  - Use the same mesh throughout
- Excellent agreement between this work and the referenced paper
air
Port 2
filling block with
variable er
air
GaAs
bridge
Port 1
GaAs
J.-S. Wang, and R. Mittra, “Finite Element Analysis of MMIC Structures and Electronic Packages Using Absorbing Boundary Conditions,” IEEE. Trans. Microwave Theory and Techniques, vol. 42, no. 3, March 1994, pp. 441-449.

---
Slotline Step
- ½ slotline on symmetry
- substrate with er=2.22
- 3rd order finite elements with 11 passes of AMR at 35 GHz with 0.001 convergence criteria
- Excellent agreement between this work and the referenced paper
slotline
air
Port 2
PEC
substrate
Port 1
|Re(E)|
35 GHz
refine
AMR + 1 frequency
K. Hirayama, Md. Alam, Y. Hayashi, and M. Koshiba, “Vector Finite Element Method with Mixed-Interpolation-Type Triangular-Prism Element for Waveguide Discontinuities,” IEEE Trans. Microwave Theory and Techniques, vol. 42, no. 12, Dec. 1994, pp. 2311-2316.

---
Microstrip Filter
- Simulation with dielectric losses only
  - conductor losses not yet supported
- 2nd order elements
- AMR with 9 iterations at 4 GHz with 0.02 convergence criteria
- Good agreement considering the differences in losses
Challenging!
refine
|Re(H)| @ 2.5 GHz
W.-C. Weng, “Design and Optimization of Compact Microstrip Wideband Bandpass Filter Using Taguchi’s Method,” IEEE Open Access Journal, vol. 10, 2022, pp. 107242-107249.

---
Regression Suites
- Automated
- With and without AMR
- OpenParEM2D
  - 27 test cases
    - Microstrip, stripline, coax, rectangular waveguide, loaded rectangular waveguide
  - 43,738 checks
- OpenParEM3D
  - 17 test cases
    - Microstrip, slotline, rectangular waveguide, loaded rectangular waveguide
    - Orientation variations (i.e. rotations in space)
  - 390 checks

---
Conclusions
- An effective 3D full-wave time-harmonic EM simulator for the calculation of S-parameters is outlined and demonstrated to produce high accuracy
- Lack of support for the gradient term on boundaries has two consequences
  - non-TE modes at ports require de-embedding (should be rare)
  - 2X run-time increase to separate forward and backward waves at the driving port due to the need to calculate H
- To Do
  - Add impedance boundary condition for losses and antennas
  - Add PML for absorbing boundary condition at ports
  - Write documentation
  - Release
size *1.5 { color white {nabla_t E_n}}

---
Thanks to LLNL’s Mark Stowell for many very helpful email exchanges.